## Slide 1
Dell recommends Windows®
Dell Vostro Desktop & Small Desktop
Model 3471 3671
Spec Sheet – September 2019
  Product appearance may vary slightly from image shown.
Notes: Revised May 8, 2017

## Slide 2
Vostro Small Desktop 3471
Features & Technical Specifications
Feature | Technical Specification
Model Number1 | 3471
Processor Options1 | Intel® Celeron® G4900 (2M Cache, 3.1 GHz) Intel® Pentium® G5400 (4M Cache, 3.7 GHz) Intel® Celeron® G4930 (2M Cache, 3.2 GHz) Intel® Pentium® Gold G5420 (4M Cache, 3.8GHz) Intel® 8th Generation Core™ i3-8100 (6M Cache, 3.6 GHz) Intel® 8th Generation Core™ i5-8400 (9M Cache, up to 4.0 GHz) Intel® 8th Generation Core™ i7-8700 (12M Cache, up to 4.6 GHz) Intel® 9th Generation Core™ i3-9100 (6M Cache, up to 4.2 GHz) Intel® 9th Generation Core™ i5-9400 (9M Cache, up to 4.1 GHz) Intel® 9th Generation Core™ i7-9700 (12M Cache, up to 4.7 GHz)
Operating System1,2 | Windows® 10 64-bit Windows® 10 64-bit Professional Windows® 10 64-bit National Academic (STF) Ubuntu
Chipset1 | Intel® B365
Graphics1,11 | Intel® UHD Graphics 610/630 with shared graphics memory (610 for PDC/CDC) NVIDIA® GeForce® GT 730 2GB GDDR5
Memory Options1,2,3 | CFL-S core i3, Pentium and Celeron up to 2400 MHz; CFL-S core i5, i7 up to 2666 MHz 4GB DDR4 (4GBx1) 8GB DDR4 (4GBx2 or 8GBx1) 12GB DDR4 (4GB+8GB) 16GB DDR4 (8GBx2 or 16GBx1) 24GB DDR4 (8GB+16GB) 32GB DDR4 (16GBx2)
UDIMM Slot | 2 UDIMM Slots
Storage Options1, 5 | 3.5” Hard Drive: 500GB, 1TB, 2TB 7200 rpm HDD 128GB, 256GB, 512GB M.2 SATA SSD Dual drive with 3.5” 1TB HDD + 128GB M.2 SATA SSD
Expansion Slots | PCIex1; PCIex16
Optical Disk Drive | Optical Disk Drive tray type 9.5mmm (optional)
Ports, Slots & Chassis1 | Front IO ports: 2x USB 3.1 Gen 1 Type-A Universal audio jack 5:1 Media card reader Rear IO ports: 4x USB 2.0 Gigabit Ethernet HDMI VGA 3-stack audio jacks supporting 5.1 surround sound
Feature | Technical Specification
Multimedia1 | Audio software: Waves MaxxAudio® Pro
Connectivity Options1 | 802.11bgn 1x1 + Bluetooth v4.0 (optional) 10/100/1000 RJ-45 Ethernet
Dimensions & Weight1,14 | Width: 92.6 (3.6”) Height: 290 (11.4”) Depth: 293mm (11.5”) Starting weight: 4.35kg (9.6 lbs)
Color Option | Black with red mesh
Security1 | Kensington Lock Slot; Padlock Loop; Microsoft Windows Bitlocker; Local HDD data wipe via BIOS ("Secure Erase"); optional Hardware TPM 2.0;
Software | My Dell, Microsoft® Office, McAfee LiveSafe (30Day), McAfee Small Business Security 30 day Trial, Dell Mobile Connect, SupportAssist
Power Supply | 200W PSU (APFC – High Voltage & Full range or EPA Bronze – Full range)
Line Voltage | 100–240 V or 200-240 V
Regulatory and Environmental Compliance1 | Energy Star 7.1 Compliant (available in selected configurations); EPEAT registered; (For specific country participation and rating please visit www.epeat.net) FCC Class B; UL; CCC; CECP/ESPL(available in selected configurations); ErP Lot 3, Tier II (effective Jan 1, 2016) which defines more stringent energy efficiency limits for the EU

## Slide 3
Vostro Desktop 3671
Features & Technical Specifications
Feature | Technical Specification
Model Number1 | 3671
Processor Options1 | Intel® Celeron® G4900 (2M Cache, 3.1 GHz) Intel® Pentium® G5400 (4M Cache, 3.7 GHz) Intel® Celeron® G4930 (2M Cache, 3.2 GHz) Intel® Pentium® Gold G5420 (4M Cache, 3.8GHz) Intel® 8th Generation Core™ i3-8100 (6M Cache, 3.6 GHz) Intel® 8th Generation Core™ i5-8400 (9M Cache, up to 4.0 GHz) Intel® 8th Generation Core™ i7-8700 (12M Cache, up to 4.6 GHz) Intel® 9th Generation Core™ i3-9100 (6M Cache, up to 4.2 GHz) Intel® 9th Generation Core™ i5-9400 (9M Cache, up to 4.1 GHz) Intel® 9th Generation Core™ i7-9700 (12M Cache, up to 4.7 GHz)
Operating System1,2 | Windows® 10 64-bit Windows® 10 64-bit Professional Windows® 10 64-bit National Academic (STF) Ubuntu
Chipset1 | Intel® B365
Graphics1,11 | Intel® UHD Graphics 610/630 with shared graphics memory (610 for PDC/CDC) NVIDIA® GeForce® GT 730 2GB GDDR5 NVIDIA® GeForce® GT 1030 2GB GDDR5 NVIDIA® GeForce® GTX 1650 4GB GDDR5 graphics memory
Memory Options1,2,3 | CFL-S core i3, Pentium and Celeron up to 2400 MHz; CFL-S core i5, i7 up to 2666 MHz 4GB DDR4 (4GBx1) 8GB DDR4 (4GBx2 or 8GBx1) 12GB DDR4 (4GB+8GB) 16GB DDR4 (8GBx2 or 16GBx1) 24GB DDR4 (8GB+16GB) 32GB DDR4 (16GBx2) 16G/32G Optane Optional
UDIMM Slot | 2 UDIMM Slots
Storage Options1, 5 | 3.5” Hard Drive: 500GB, 1TB, 2TB 7200rpm HDD 128GB, 256GB, 512GB M.2 PCIe SSD Dual drive with 3.5” 1TB 7200 rpm HDD + 128GB PCIe M.2 SSD
Expansion Slots | Parallel/Serial add-in card (FH) (optional) PCIex16 FH; PCIex1 X2 FH; PCIx1(only available on Silver mesh unit)
Optical Disk Drive | Optical Disk Drive tray type 9.5mmm (optional)
Feature | Technical Specification
Ports, Slots & Chassis1 | Front IO ports: 2x USB 3.1 Gen 1 Type-A Universal audio jack 5:1 Media card reader Rear IO ports: 4x USB 2.0 Gigabit Ethernet HDMI VGA 3-stack audio jacks supporting 5.1 surround sound
Multimedia1 | Audio software: Waves MaxxAudio® Pro
Connectivity Options1 | 802.11bgn 1x1 + Bluetooth v4.0 (optional) 10/100/1000 RJ-45 Ethernet
Dimensions & Weight1,14 | Width: 160mm (6.3”) Height: 373.7mm (14.7”) Depth: 289.4mm (11.4”) Starting Weight: 5.27kg (11.6 lbs)
Color Option | Black with red mesh / Black with silver mesh
Security1 | Kensington Lock Slot; Padlock Loop; Microsoft Windows Bitlocker; Local HDD data wipe via BIOS ("Secure Erase"); optional Hardware TPM 2.0;
Software | My Dell, Microsoft® Office, McAfee LiveSafe (30Day), McAfee Small Business Security 30 day Trial, Dell Mobile Connect, SupportAssist
Power Supply | 290W PSU (APFC – Full range or EPA Bronze – Full range)
Line Voltage | 100–240 VAC, 50–60Hz
Regulatory and Environmental Compliance1 | Energy Star 7.1 Compliant (available in selected configurations); EPEAT registered; (For specific country participation and rating please visit www.epeat.net) FCC Class B; UL; CCC; CECP/ESPL; (available in selected configurations) ErP Lot 3, Tier II (effective Jan 1, 2016) which defines more stringent energy efficiency limits for the EU

## Slide 4: Optional Vostro accessories
You can maximize the versatility and performance of your Vostro Family Desktops with Dell recommended accessories to get the best user experience for your business needs.
Dell 22 Monitor – P2219H
Optimize your workspace with this efficient 21.5" monitor built with an ultrathin bezel design, a small footprint and comfort-enhancing features.
Keyboard and Mouse Combo – KM636
Keep you desk clutter-free with a wireless keyboard and mouse combo, featuring spacious chiclet keyboard with multi-media keys and reduced key gaps for minimal dust accumulation.
  Product appearance may vary slightly from image shown.
  Optional accessories shown subject to regional availability.
Dell Pro Stereo Headset – UC150 – Skype for Business
Experience great audio clarity whether you're on a conference call or listening to your favorite music. Enjoy optimized in-person call quality and music clarity with HD wideband voice and a dynamic equalizer.
Dell Wireless Mouse - WM126
Travel light with a compact, wireless mouse with optical tracking and long battery life. (available in red, blue, white & blk).